## Slide 1: Application Layer
COMPSCI 453 Computer Networks
Professor Jim Kurose
College of Information and Computer Sciences
University of Massachusetts
Class textbook:
Computer Networking: A Top-Down Approach (8th ed.)
J.F. Kurose, K.W. Ross
Pearson, 2020
http://gaia.cs.umass.edu/kurose_ross
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System: DNS
P2P applications
video streaming, CDNs
socket programming with UDP and TCP

## Slide 2: DNS: Domain Name System
people: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., cs.umass.edu - used by humans
Q: how to map between IP address and name, and vice versa ?
Domain Name System (DNS):
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, DNS servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 3: DNS: services, structure
Q: Why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
DNS services:
hostname-to-IP-address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name
A: doesn‘t scale!
Comcast DNS servers alone: 600B DNS queries/day
Akamai DNS servers alone: 2.2T DNS queries/day

## Slide 4: Thinking about the DNS
humongous distributed database:
~ billion records, each simple
handles many trillions of queries/day:
many more reads than writes
performance matters: almost every Internet transaction interacts with DNS - msecs count!
organizationally, physically decentralized:
millions of different organizations responsible for their records
“bulletproof”: reliability, security

## Slide 5: DNS: a distributed, hierarchical database
Client wants IP address for www.amazon.com; 1st approximation:
client queries root server to find .com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
.com DNS servers
.org DNS servers
.edu DNS servers
…
…
Top Level Domain
Root DNS Servers
Root
nyu.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
Authoritative
…
…
…
…

## Slide 6: DNS: root name servers
official, contact-of-last-resort by name servers that can not resolve name

## Slide 7: DNS: root name servers
official, contact-of-last-resort by name servers that can not resolve name
incredibly important Internet function
  Internet couldn’t function without it!
  DNSSEC – provides security (authentication, message integrity)
ICANN (Internet Corporation for Assigned Names and Numbers) manages root DNS domain
13 logical root name “servers” worldwide each “server” replicated many times (~200 servers in US)

## Slide 8: Top-Level Domain, and authoritative servers
Top-Level Domain (TLD) servers:
  responsible for .com, .org, .net, .edu, .aero, .jobs, .museums, and all top-level country domains, e.g.: .cn, .uk, .fr, .ca, .jp
  Network Solutions: authoritative registry for .com, .net TLD
  Educause: .edu TLD
authoritative DNS servers:
  organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider

## Slide 9: Local DNS name servers
when host makes DNS query, it is sent to its local DNS server
  Local DNS server returns reply, answering:
    from its local cache of recent name-to-address translation pairs (possibly out of date!)
    forwarding request into DNS hierarchy for resolution
  each ISP has local DNS name server; to find yours:
    MacOS: % scutil --dns
    Windows: >ipconfig /all
local DNS server doesn’t strictly belong to hierarchy

## Slide 10: DNS name resolution: iterated query
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu
Iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 11: DNS name resolution: recursive query
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu

## Slide 12: Caching DNS Information
once (any) name server learns mapping, it caches mapping, and immediately returns a cached mapping in response to a query
  caching improves response time
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
cached entries may be out-of-date
  if named host changes IP address, may not be known Internet-wide until all TTLs expire!
  best-effort name-to-address translation!

## Slide 13: DNS records
DNS: distributed database storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A
  name is hostname
  value is IP address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really servereast.backup2.ibm.com
  value is canonical name
type=MX
  value is name of SMTP mail server associated with name

## Slide 14: DNS protocol messages
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
DNS query and reply messages, both have same format:
message header:
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative

## Slide 15: DNS protocol messages
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
DNS query and reply messages, both have same format:
name, type fields for a query
RRs in response to query
records for authoritative servers
additional “ helpful” info that may be used

## Slide 16: Getting your info into the DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts NS, A RRs into .com TLD server:
  (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server locally with IP address 212.212.212.1
  type A record for www.networkuptopia.com
  type MX record for networkutopia.com

## Slide 17: DNS security
DDoS attacks
bombard root servers with traffic
  not successful to date
  traffic filtering
  local DNS servers cache IPs of TLD servers, allowing root server bypass
bombard TLD servers
  potentially more dangerous
Spoofing attacks
intercept DNS queries, returning bogus replies
  DNS cache poisoning
  RFC 4033: DNSSEC authentication services

## Slide 18
COMPSCI 453 Computer Networks
Professor Jim Kurose
College of Information and Computer Sciences
University of Massachusetts
Class textbook:
Computer Networking: A Top-Down Approach (8th ed.)
J.F. Kurose, K.W. Ross
Pearson, 2020
http://gaia.cs.umass.edu/kurose_ross
Video: 2020, J.F. Kurose, All Rights Reserved
Powerpoint: 1996-2020, J.F. Kurose, K.W. Ross, All Rights Reserved
Application Layer
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System: DNS
P2P applications
video streaming, CDNs
socket programming with UDP and TCP