## Slide 1: Elements of 4G LTE architecture
Mobile device
(UE)
Base station
(eNode-B)
radio access
network
all-IP Enhanced Packet Core (EPC)
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
to
Internet
…
Mobile device:
smartphone, tablet, laptop, IoT, ... with 4G LTE radio
64-bit International Mobile Subscriber Identity (IMSI), stored on SIM (Subscriber Identity Module) card
LTE jargon: User Equipment (UE)

## Slide 2: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Base station:
at “edge” of carrier’s network
manages wireless radio resources, mobile devices in its coverage area (“cell”)
coordinates device authentication with other elements
similar to WiFi AP but:
  active role in user mobility
  coordinates with nearly base stations to optimize radio use
LTE jargon: eNode-B

## Slide 3: Radio Access Network: 4G radio
connects device (UE) to a base station (eNode-B)
  multiple devices connected to each base station
many different possible frequencies bands, multiple channels in each band
  popular bands: 600, 700, 850, 1500, 1700, 1900, 2100, 2600, 3500 MHz
  separate upstream and downstream channels
sharing 4G radio channel among users:
  OFDM: Orthogonal Frequency Division Multiplexing
  combination of FDM, TDM
100’s Mbps possible per user/device
Mobile device
(UE)
Base station
(eNode-B)
Notes: G-defined subbands are narrow (e.g., 15 kHz)

## Slide 4: Spectrum
CBRS
Notes: 8 orders of magnitude: 9 Khz to 300 Ghz

## Slide 5: OFDMA: time division (LTE)
Subcarrier frequencies
time (symbols)

## Slide 6: OFDMA: time division (LTE)
time to transmit one OFDM symbol on subcarrier frequency
Physical Resource Block (PRB ): blocks of 7x12=84 resource elements
unit of transmission scheduling
Subcarrier frequencies

## Slide 7: OFDMA:
Subcarrier frequencies
time (symbols)
PRB
PRB
Transmission Time Interval (TTI): 1 ms
Transmission scheduling example:
Send to 7 UEs in 7 blocks of REs in one PRB
UE1
UE2
UE3
UE4
UE5
UE6
UE7

## Slide 8: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Home Subscriber Service
stores info about mobile devices for which the HSS’s network is their “home network”
works with MME in device authentication

## Slide 9: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Serving Gateway (S-GW), PDN Gateway (P-GW)
lie on data path from mobile to/from Internet
P-GW
  gateway to mobile cellular network
  Looks like nay other internet gateway router
  provides NAT services
other routers:
  extensive use of tunneling

## Slide 10: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Mobility Management Entity
device authentication (device-to-network, network-to-device) coordinated with mobile home network HSS
mobile device management:
  device handover between cells
  tracking/paging device location
path (tunneling) setup from mobile device to P-GW

## Slide 11: LTE: data plane control plane separation
control plane
new protocols for mobility management , security, authentication (later)
MME
HSS
base station
P-GW
S-GW
base station
P-GW
S-GW
data plane
new protocols at link, physical layers
IP tunnels
extensive use of tunneling to facilitate mobility

## Slide 12: LTE data plane protocol stack: first hop
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
data
plane
P-GW
S-GW
Application
Transport
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Link
base station
LTE link layer protocols:
Packet Data Convergence: header compression, encryption
Radio Link Control (RLC) Protocol: fragmentation/reassembly, reliable data transfer
Medium Access: requesting, use of radio transmission slots (OFDM)

## Slide 13: LTE data plane protocol stack: packet core
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
P-GW
S-GW
base station
\
tunneling:
mobile datagram encapsulated using GPRS Tunneling Protocol (GTP), sent inside UDP datagram to S-GW
S-GW re-tunnels datagrams to P-GW
supporting mobility: only tunneling endpoints change when mobile user moves

## Slide 14: LTE data plane: associating with a BS
data
plane
P-GW
S-GW
base station
BS broadcasts primary synch signal every 5 ms on all frequencies
BSs from multiple carriers may be broadcasting synch signals
1
mobile finds a primary synch signal, then locates 2nd synch signal on this freq.
mobile then finds info broadcast by BS: channel bandwidth, configurations; BS’s cellular carrier info
mobile may get info from multiple base stations, multiple cellular networks
2
mobile selects which BS to associate with (e.g., preference for home carrier)
3
more steps still needed to authenticate, establish state, set up data plane
4
1
2
3

## Slide 15: LTE mobiles: sleep modes
data
plane
ZZZZ...
as in WiFi, Bluetooth: LTE mobile may put radio to “sleep” to conserve battery:
light sleep: after 100’s msec of inactivity
  wake up periodically (100’s msec) to check for downstream transmissions
deep sleep: after 5-10 secs of inactivity
  mobile may change cells while deep sleeping – need to re-establish association

## Slide 16: Global cellular network: a network of IP networks
…
visited mobile
carrier network
…
public Internet
and
inter-carrier IPX
…
P-GW
P-GW
home mobile
carrier network
Home
Subscriber
Server
in home network
roaming in visited network
SIM card: global identify info in home network
all IP:
carriers interconnect with each other, and public internet at exchange points
legacy 2G, 3G: not all IP, handled otherwise
home network HSS:
identify & services info, while in home network and roaming