## Slide 1: Broadcast routing
R1
R2
R3
R4
source duplication
R1
R2
R3
R4
in-network
duplication
duplicate
creation/transmission
duplicate
duplicate
deliver packets from source to all other nodes
source duplication is inefficient:
source duplication: how does source determine recipient addresses?

## Slide 2: In-network duplication
flooding: when node receives broadcast packet, sends copy to all neighbors
  problems: cycles & broadcast storm
controlled flooding: node only broadcasts pkt if it hasn’t broadcast same packet before
  node keeps track of packet ids already broadacsted
  or reverse path forwarding (RPF): only forward packet if it arrived on shortest path between node and source
spanning tree:
  no redundant packets received by any node

## Slide 3: Spanning tree
A
B
G
D
E
c
F
A
B
G
D
E
c
F
(a) broadcast initiated at A
(b) broadcast initiated at D
first construct a spanning tree
nodes then forward/make copies only along spanning tree

## Slide 4: Spanning tree: creation
A
B
G
D
E
c
F
1
2
3
4
5
stepwise construction of spanning tree (center: E)
A
B
G
D
E
c
F
(b) constructed spanning tree
center node
each node sends unicast join message to center node
  message forwarded until it arrives at a node already belonging to spanning tree

## Slide 5: Multicast routing: problem statement
goal: find a tree (or trees) connecting routers having local mcast group members
tree: not all paths between routers used
shared-tree: same tree used by all group members
shared tree
source-based trees
group
member
not group
member
router
with a
group
member
router
without
group
member
legend
source-based: different tree from each sender to rcvrs
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-9

## Slide 6: Approaches for building mcast trees
approaches:
source-based tree: one tree per source
  shortest path trees
  reverse path forwarding
group-shared tree: group uses one tree
  minimal spanning (Steiner)
  center-based trees
…we first look at basic approaches, then specific protocols adopting these approaches
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-11

## Slide 7: Shortest path tree
mcast forwarding tree: tree of shortest path routes from source to all receivers
  Dijkstra’s algorithm
i
router with attached
group member
router with no attached
group member
link used for forwarding,
i indicates order link
added by algorithm
LEGEND
R1
R2
R3
R4
R5
R6
R7
2
1
6
3
4
5
s: source
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-12

## Slide 8: Reverse path forwarding
if (mcast datagram received on incoming link on shortest path back to center)
then flood datagram onto all outgoing links
else ignore datagram
rely on router’s knowledge of unicast shortest path from it to sender
each router has simple forwarding behavior:
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-13

## Slide 9: Reverse path forwarding: example
result is a source-specific reverse SPT
  may be a bad choice with asymmetric links
router with attached
group member
router with no attached
group member
datagram will be forwarded
LEGEND
R1
R2
R3
R4
R5
R6
R7
s: source
datagram will not be
forwarded
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-14

## Slide 10: Reverse path forwarding: pruning
forwarding tree contains subtrees with no mcast group members
  no need to forward datagrams down subtree
  “prune” msgs sent upstream by router with no downstream group members
router with attached
group member
router with no attached
group member
prune message
LEGEND
links with multicast
forwarding
P
R1
R2
R3
R4
R5
R6
R7
s: source
P
P
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-15

## Slide 11: Shared-tree: steiner tree
steiner tree: minimum cost tree connecting all routers with attached group members
problem is NP-complete
excellent heuristics exists
not used in practice:
  computational complexity
  information about entire network needed
  monolithic: rerun whenever a router needs to join/leave
Notes: Notes:
1. See L. Wei and D. Estrin, “A Comparison of multicast trees and algorithms,” TR USC-CD-93-560, Dept. Computer Science, University of California, Sept 1993 for a comparison of heuristic approaches.
3.3 Network Layer: Multicast Routing Algorithms 3-16

## Slide 12: Center-based trees
single delivery tree shared by all
one router identified as “center” of tree
to join:
  edge router sends unicast join-msg addressed to center router
  join-msg “processed” by intermediate routers and forwarded towards center
  join-msg either hits existing tree branch for this center, or arrives at center
  path taken by join-msg becomes new branch of tree for this router
Notes: Notes:
1. It’s always nice to see a PhD dissertation with impact. The earliest discussion of center-based trees for multicast appears to be D. Wall, “Mechanisms for Broadcast and Selective Broadcast,” PhD dissertation, Stanford U., June 1980.
3.3 Network Layer: Multicast Routing Algorithms 3-17

## Slide 13: Center-based trees: example
suppose R6 chosen as center:
router with attached
group member
router with no attached
group member
path order in which join messages generated
LEGEND
2
1
3
1
R1
R2
R3
R4
R5
R6
R7
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-18

## Slide 14: Internet Multicasting Routing: DVMRP
DVMRP: distance vector multicast routing protocol, RFC1075
flood and prune: reverse path forwarding, source-based tree
  RPF tree based on DVMRP’s own routing tables constructed by communicating DVMRP routers
  no assumptions about underlying unicast
  initial datagram to mcast group flooded everywhere via RPF
  routers not wanting group: send upstream prune msgs
Notes: Notes:
D. Waitzman, S. Deering, C. Partridge, “Distance Vector Multicast Routing Protocol,” RFC 1075, Nov. 1988. The version of DVMRP in use today is considerably enhanced over the RFC1075 spec.
A more up-to-date “work-in-progress” defines a version 3 of DVMRP: T. Pusateri, “Distance Vector Multicast Routing Protocol,” work-in-progress, draft-ietf-idmr-v3-05.ps
3.4 Network Layer: Internet Multicast Routing Algorithms 3-20

## Slide 15: DVMRP: continued…
soft state: DVMRP router periodically (1 min.) “forgets” branches are pruned:
  mcast data again flows down unpruned branch
  downstream router: reprune or else continue to receive data
routers can quickly regraft to tree
  following IGMP join at leaf
odds and ends
  commonly implemented in commercial router
Notes: Notes:
1. See www.mbone.com/mbone/routers.html for a (slightly outdatet) list of multicast capable routers (supporting DVMPR as well as other protocols) from various vendors.
2. ftp://parcftp.xerox.com/pub/net-research/ipmulti for circa 1996 public copy “mrouted” v3.8 of DVMRP routing software for various workstation routing platforms.
3.4 Network Layer: Internet Multicast Routing Algorithms 3-21

## Slide 16: Tunneling
Q: how to connect “islands” of multicast routers in a “sea” of unicast routers?
mcast datagram encapsulated inside “normal” (non-multicast-addressed) datagram
normal IP datagram sent thru “tunnel” via regular IP unicast to receiving mcast router (recall IPv6 inside IPv4 tunneling)
receiving mcast router unencapsulates to get mcast datagram
physical topology
logical topology
Notes: Notes:
For a general discussion of IP encapsulation, see C. Perkins, “IP Encapsulation within IP,” RFC 2003, Oct. 1996.
The book S. Bradner, A Mankin, “Ipng: Internet protocol next generation,” Addison Wesley, 1995 has a very nice discussion of tunneling
Tunneling can also be used to connect islands of IPv6 capable routers in a sea IPv4 capable routers. The long term hope is that the sea evaporates leaving only lands of IPv6!
3.4 Network Layer: Internet Multicast Routing Algorithms 3-22

## Slide 17: PIM: Protocol Independent Multicast
not dependent on any specific underlying unicast routing algorithm (works with all)
two different multicast distribution scenarios :
dense:
group members densely packed, in “close” proximity.
bandwidth more plentiful
sparse:
# networks with group members small wrt # interconnected networks
group members “widely dispersed”
bandwidth not plentiful
Notes: Notes:
a very readable discussion of the PIM architecture is S. Deering, D. Estrin, D. Faranacci, V. Jacobson, C. Liu, L. Wei, “The PIM Architecture for Wide Area Multicasting,” IEEE/ACM Transactions on Networking, Vol. 4, No. 2, April 1996.
D. Estrin et al, PIM-SM: Protocol Specification, RFC 2117, June 1997
S. Deering et al, PIM Version 2, Dense Mode Specification, work in progress, draft-ietf-idmr-pim-dm-05.txt
PIM is implemented in Cisco routers and has been deployed in UUnet as part of their streaming multimedia delivery effort. See S. LaPolla, “IP Multicast makes headway among ISPs,” PC Week On-Line, http://www.zdnet.com/pcweek/news/1006/06isp.html
3.4 Network Layer: Internet Multicast Routing Algorithms 3-25

## Slide 18: Consequences of sparse-dense dichotomy:
dense
group membership by routers assumed until routers explicitly prune
data-driven construction on mcast tree (e.g., RPF)
bandwidth and non-group-router processing profligate
sparse:
no membership until routers explicitly join
receiver- driven construction of mcast tree (e.g., center-based)
bandwidth and non-group-router processing conservative
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-26

## Slide 19: PIM- dense mode
flood-and-prune RPF: similar to DVMRP but…
underlying unicast protocol provides RPF info for incoming datagram
less complicated (less efficient) downstream flood than DVMRP reduces reliance on underlying routing algorithm
has protocol mechanism for router to detect it is a leaf-node router
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-27

## Slide 20: PIM - sparse mode
center-based approach
router sends join msg to rendezvous point (RP)
  intermediate routers update state and forward join
after joining via RP, router can switch to source-specific tree
  increased performance: less concentration, shorter paths
all data multicast
from rendezvous
point
rendezvous
point
join
join
join
R1
R2
R3
R4
R5
R6
R7
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-28

## Slide 21: PIM - sparse mode
sender(s):
unicast data to RP, which distributes down RP-rooted tree
RP can extend mcast tree upstream to source
RP can send stop msg if no attached receivers
  “no one is listening!”
all data multicast
from rendezvous
point
rendezvous
point
join
join
join
R1
R2
R3
R4
R5
R6
R7
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-29